## Slide 1: Capstone Project Phase B 24-1-D-28
Supervisors:
Dr. Anat Dahan
Dr. Marcela Viviana Karpuj
Students:
Michael Malka 311446231
Nir Asulin 305221483
01

## Slide 2: TABLE OF CONTENTS
02
03 | Introduction
04 | Motivation
05 | System Requirements
06 | Our Solution
07 | CSV file analysis algorithm
08 | Technologies Used
09 | Challenges
10 | Test Plan
11 | Our Key Achievements
12 | Demo
13 - 17 | Results
18 | Future Work

## Slide 3: Introduction
03
Parkinson's disease (PD) affects millions globally and is marked by tremors, slowness, stiffness, and instability.
Early diagnosis is difficult due to subtle symptoms, but motor asymmetry (more severe symptoms on one side) can signal early PD.
Our project uses VR technology to detect these early motor and cognitive impairments.

## Slide 4: Motivation
Improve patient experience in diagnostic experiences and compliance
Enhance early diagnostic accuracy
Enhancing Neurological Healthcare through Technology
Potential for use in other neurological diagnostics and rehabilitation
04

## Slide 5: System Requirements
The system must detect hand movement asymmetry accurately during a virtual swimming task.
Data on hand movements (position, rotation, timing, velocity and stroke events) must be recorded for later analysis.
The interface should be user-friendly for both patients and clinicians, minimizing training time.
The system should run smoothly on the Oculus Quest 2 and provide real-time feedback during the test.
05

## Slide 6: Our Solution
VR-Based Detection
VR system that tracks user movements, detecting asymmetries indicative of early PD.
Simulates swimming tasks using the Oculus Quest 2 and designed in Unity game engine.
Records data in CSV format for detailed analysis.
06

## Slide 7: CSV file analysis algorithm
07
,L and R are the measurements of left and right hand, respectively.
, threshold value for asymmetry.
, then the patient is considered to have asymmetry in that measurement.

## Slide 8: Technologies Used
Oculus Quest 2
VR hardware for immersive user interaction and hand-tracking capabilities.
Haptics for feedback during the swimming simulation.
Visual Studio 2022
Development environment for coding and debugging Unity C# scripts.
Python (Google Colab)
Used for data analysis and post-processing of hand movement data (CSV files).
Unity Game Engine
For creating the virtual reality environment and simulating hand movement.
Integration with the Oculus Quest 2 through the Oculus Integration SDK.
08

## Slide 9
12

## Slide 10: Test Plan
# | Test Case | Expected results | status
1 | VR_environment_launches | The VR environment should open successfully and be visible through the VR headset. | Pass
2 | User_input | User enters their name, and the “Start” button is enabled. | Pass
3 | Start_simulation | The timer is visible and counts down from 2 minutes during the simulation and start only when the first swimming motion is performed. | Pass
4 | Display_timer_in_simulation | The timer is visible and counts down from 2 minutes during the simulation and start only when the first swimming motion is performed. | Pass
5 | Hand_tracking_during_swimming | Hand movements are tracked in real-time without delays. | Pass
6 | Simulation_time_limit | The simulation ends automatically after 02:00 minutes, and swimming is no longer possible. | Pass
7 | System_performance | VR system operates smoothly with no frame drops or glitches. | Pass
8 | User_feedback | Users hear appropriate sound effects when interacting with the simulation (e.g., water entry and swimming motions). | Pass
9 | Save_data_to_CSV | The movement data (x y z positions, rotations etc) is successfully saved in a CSV file. | Pass
10 | CSV_file_import | The saved CSV file can be successfully imported and used for analysis. | Pass
10

## Slide 11: Results
13
- The CSV saved in Quest 2, Then we export it into the computer
- The name “demo user” is saved with the current date and time “2024/10/08 at 15:24”

## Slide 12: Results
14
CSV Recording of Demo User

## Slide 13: Results
15
First Asymmetry Test
Second Asymmetry Test
Both tests exceed the threshold suggesting that the test subjects may be at risk for PD

## Slide 14: Results
16
Threshold Visualization:
Blue line: Subject's IA values
Red dashed line: Healthy threshold
IA Comparison:
Subject's IA values for hand positions are significantly higher than healthy thresholds.
Persistent Asymmetry:
Elevated IA values sustained across time during the simulation.
Diagnostic Insight:
Indicates notable hand movement asymmetry—key marker for potential motor impairment.

## Slide 15
VR Diagnostic Tool
Movement Analysis Algorithm
Automated Data Capture & Analysis
User-Centric Design
Created a VR system simulating swimming actions for detecting subtle motor asymmetries, early indicators of PD.
Built with Oculus Quest 2 and Unity for a responsive and immersive diagnostic experience.
Real-time hand movement tracking, calculating the Index of Asymmetry (IA).
Captures and analyzes movement data for PD markers.
Intuitive, comfortable VR experience for accurate diagnostics.
Our Key Achievements
11

## Slide 16
Data Collection Bugs
Collider Implementation
Early issues with capturing precise movement data (timestamps, positions, rotations) in CSV files. Resolved through debugging.
Added colliders and boundaries to prevent users from passing through objects or leaving the virtual environment.
Simplified materials, adjusted graphics quality, and optimized scene rendering for smooth performance on the Quest 2.
Optimization for Oculus Quest 2
Challenges
09

## Slide 17: Future Work
Enhanced Simulation
Add sea animals and water conditions for realism and better data.
Hand-Tracking
Use hand tracking for more precise measurements.
Real Time Feedback Provide immediate feedback with visual cues and haptics.
Machine Learning
Apply AI to improve disease prediction.
Expanded Research
Test with more patients and study other diseases.
Wearables
Integrate devices to track more physiological data.
Improved Algorithm Make asymmetry detection more accurate.
Cloud Storage
Enable secure, remote access to data for collaboration.
18

## Slide 18: Any Questions?
19

## Slide 19: Thank You For Listening
Github Repository
20